## Slide 1: ECE4560 – Introduction to Automation and Robotics
Rigid Bodies: An Introduction
Patricio A. Vela

## Slide 2: Rigid Bodies: Core Principles
The mathematical description of rigid bodies and their movement falls out from a few simple principles. Let’s review these.

## Slide 3: Definition of a Rigid Body
Definition. A rigid body is a collection of points/particles which have a fixed physical relationship amongst themselves.
Alternatively put, objects whose particles can shift relative to each other are deformable and therefore not rigid.

## Slide 4: Definition of a Rigid Body Motion
Definition. A rigid body motion describes how the individual particles of a rigid body move as a function of time.
Equivalently, a rigid body motion is the motion of a body fixed reference frame.

## Slide 5: Definition of a Displacement/Transformation
Definition. A displacement/transformation is the movement of a rigid body without reference to time.
- From some frame to but without knowing time.

## Slide 6: Degrees of Freedom of a Motion
Definition. The degrees of freedom (DOF) of a rigid body motion is the minimal number of independent variables needed to uniquely specify the motion of an object.
Why important?
The representations we will use to describe robot frames will usually employ more variables than the degrees of freedom.
However, the velocities of robot frames will always have a compact vector form whose dimension is equal to the DOF.

## Slide 7: Degrees of Freedom for Planar Rigid Body Motion
Also sometimes just called 2D rigid body motion.

## Slide 8: Degrees of Freedom for Spatial Rigid Body Motion
Usually called 3D rigid body motion.