## Slide 1: ECE4560 – Introduction to Automation and Robotics
Lie Groups: Quick Intro to Matrix Versions
Patricio A. Vela

## Slide 2: What is a group?
Definition. A group is a mathematical structure consisting of a set of elements that can be indexed; the set can be finite, infinite, or continuous. Denote this set of elements by , for the index set. The group has
1) An associative group operation, denoted by , called the group product.
2) A unique element, , called the identity element, such that
3) An inverse element for every called the inverse, for which

## Slide 3: What is a Lie group?
Definition. A Lie group is a group which is also a smooth manifold and for which the group product and inverse are smooth.
OK, but what …
is smooth?
is a manifold?

## Slide 4: Example: Rotation matrices (i.e., Orthogonal matrices)
Definition. The Lie group consists of the set of orthogonal 2x2 matrices. It is called the orthogonal group in 2-space.
Definition. The Lie group consists of the set of orthogonal 2x2 matrices with unit determinant. It is called the special rthogonal group in 2-space.
such that it comprises of and
can be represented by , such that

## Slide 5: Example: Rotation matrices (i.e., Orthogonal matrices)
Definition. The Lie group consists of the set of orthogonal 3x3 matrices. It is called the orthogonal group in 3-space.
Definition. The Lie group consists of the set of orthogonal 3x3 matrices with unit determinant. It is called the special orthogonal group in 3-space.
such that it comprises of and

## Slide 6: Example: Rotation matrices (i.e., Orthogonal matrices)
Definition. The Lie group consists of the set of 2D translations. It is called Euclidean 2-space.
Definition. The Lie group consists of the set of 2D rigid body displacements. It is called the special Euclidean group in 2-space.
can be represented by , such that
can be represented by ,
where and

## Slide 7: Example: Rotation matrices (i.e., Orthogonal matrices)
Definition. The Lie group consists of the set of 3D translations. It is called Euclidean 3-space.
Definition. The Lie group consists of the set of 2D rigid body displacements. It is called the special Euclidean group in 3-space.
can be represented by ,
where and
can be represented by , such that

## Slide 8: The Space
Consider a 3D rigid body that is free to rotate about a fixed point in it.
Let there be a frame located at the fixed point.
Applying the rotation to the body changes the location of points but keeps the point at the frame origin at the frame origin.
However, all points should preserve their mutual relationships.